## Slide 1
2-AXIS SELF-STABILIZING SPOON
ASSISTING PEOPLE WITH PARKINSON’S DISEASE
Presented by:
TEAM: WeMakeIt
  Hiran Dharmapala
  Nimesha Nanayakkara
  Lasindu Viduranga
University of Sri Jayewardenepura, Sri Lanka

## Slide 2
The Challenge of Parkinson’s Tremors
  Parkinson’s Disease affects millions, leading to uncontrollable hand tremors.
  Tremors make basic tasks like eating very difficult.
OUR GOAL: HELP INDIVIDUALS EAT WITH DIGNITY AND LESS FRUSTRATION.

## Slide 3
1
2
3
OUR ASSISTIVE INNOVATION
A 2-axis self-stabilizing spoon that detects hand tremors.
Automatically counters motion to reduce food spillage.
Affordable, compact, and customizable for real-life use.

## Slide 4
COMPONENTS:
  Arduino Nano
  MPU6050 (Gyroscope + Accelerometer)
  2 × SG90 Servo Motors
  3D Spoon Structure
  2 × 3.7 V 800mAh Lipo Batteries + Power Circuit
WORKING PRINCIPLE:
  MPU6050 tracks hand motion (pitch and roll).
  Arduino processes the data with filtering.
  Servos move the spoon in opposite directions to stabilize it.
Component List & Working Principle
Arduino Nano
MPU6050 (Gyroscope + Accelerometer)
2 × SG90 Servo Motors

## Slide 5
The Science Behind It
COMPLEMENTARY FILTER
  Angle = (1 - α) * Accel + α * Gyro
ROTATION THEORY
  Avoids gimbal lock.
MECHANICAL ISOLATION:
  Designed to isolate spoon from hand motion using 2-axis articulation
CIRCUIT DIAGRAM
  This circuit connects an Arduino Nano to an MPU6050 sensor and two servo motors, powered by 2 × 3.7V 800mAh Lipo Batteries. The MPU6050 provides motion data, while the servos respond based on sensor input. Ideal for balance or motion-controlled projects.

## Slide 6
Final Overview
  Provides tremor compensation using real-time feedback.
  Improves quality of life during meals.
  Simple electronics + 3D design = practical, low-cost solution.
.
Future plans: Sleeker design, faster motors, rechargeable battery.

## Slide 7
Overcoming a Major Obstacle
CHALLENGE
Sudden hand jerks caused servo overshoot and instability.
Implemented a complementary filter to smooth sensor readings,
ensuring stable and responsive spoon motion.
SOLUTION

## Slide 8
To enhance the design, we plan to:
Replace SG90 servos with MG90S for faster response.
Explore DC or stepper motors for precision.
Reduce the size for better comfort.
Switch from a bulky 3.7V 800mAh Lipo Battery to a more light weight and small one, making the device user-friendly.

## Slide 9
About Us
Hiran Dharmapala
Nimesha Nanayakkara
Lasindu Viduranga
Institution:
University of Sri Jayewardenepura, Sri Lanka
We’re proud to offer a low-cost innovation to assist those affected by Parkinson’s.
Engineering with purpose.
“WEMAKEIT”